## Slide 1: Efficient ADCs in nano-scale CMOS Technology
Carsten Wulff

## Slide 2
  Motivation
    Reduced power supply in nano-scale CMOS
    Reduced output resistance in nano-scale CMOS
  New switched-capacitor sigma-delta architecture
    Paper 1 & 2: Open-loop sigma delta modulators (OLSDM)
    Paper 3: Resonators in OLSDM
  Replacing OTAs
    Paper 4: Comparators in 90nm
    Paper 5: Switched open-loop pipelined stage
    Paper 6 & 7: Comparator based switched-capacitor circuits

## Slide 3
Reduced supply voltage
From ITRS roadmap [http://www.itrs.net]

## Slide 4
In short: A high accuracy systems require huge capacitors in nano-scale CMOS
Increased capacitance
Chart: Supply Voltage
| 0.65 | 1.0 | 1.2 | 1.8 | 2.5 | 3.3
 | 232.1284 | 98.0742 | 68.1071 | 30.2698 | 15.6919 | 9.0059
B=14, T=80o

## Slide 5
Reduced output resistance leads to reduced intrinsic gain
Simulations in SPICE using W/L = 10, VEFF = VDD/8, VDS =VDD/2,L = 1.2Lmin.
Chart: Technology Node [nm]
| 350.0 | 180.0 | 130.0 | 90.0 | 65.0
"Intrinsic Gain" | 35.672 | 28.235 | 24.557 | 22.2 | 15.46

## Slide 6
Operational transconductance amplifier gain
dB
Chart: Technology Node [nm]
| 350.0 | 180.0 | 130.0 | 90.0 | 65.0
Common Source | 29.672 | 22.235 | 18.557 | 16.2 | 9.46
Folded Cascode | 65.344 | 50.47 | 43.114 | 38.4 | 24.92
Two-Stage (FC +CS) | 95.016 | 72.705 | 61.671 | 54.6 | 34.38
10-bit limit | 66 | 66 | 66 | 66 | 66 | 66 | 66

## Slide 7
Increased Capacitance
Solution : Use oversampling – Sigma-Delta Modulators (Papers 1, 2 & 3)
Reduced OTA gain
Solution: Replace OTAs
(Papers (4), 5, 6, 7)

## Slide 8: New Switched-Capacitor Sigma-Delta Architecture

## Slide 9
Paper 1: Analog Modulo Integrator For Use In Open-Loop Sigma-Delta Modulators
    Carsten Wulﬀ, Øystein Knauserud, Trond Ytterdal, In proceedings of the 24th NORCHIP Conference, 2006. Nov. 2006 Pages 125 - 128 Digital Object Identiﬁer 10.1109/NORCHP.2006.329259
In short: Introduces the switched capacitor analog modulo integrator

## Slide 10
Paper 2: Switched Capacitor Analog Modulo Integrator For Application In Open Loop Sigma-Delta Modulators
    Carsten Wulﬀ, Øystein Knauserud, Trond Ytterdal, Analog Integrated Circuits and Signal Processing Springer Netherlands, ISSN 0925-1030, Volume 54, Number 2, Pages 121-131, Febuary 2008 DOI 10.1007/s10470-007-9084-2
In short: Discusses error sources and presents more thorough simulations

## Slide 11
Paper 3: Resonators In Open-Loop Sigma-Delta Modulators
    Carsten Wulﬀ and Trond Ytterdal, Submitted to IEEE Transactions on Circuits and Systems I: Regular papers
In short: Introduces modulo resonators and proves input signal restrictions

## Slide 12
The modulo resonator

## Slide 13
A fifth order 8-bit OSR=4 open-loop sigma-delta modulator

## Slide 14: Replace OTAs

## Slide 15
Paper 4: 0.8V 1GHz Dynamic Comparator In Digital 90nm CMOS Technology
    Carsten Wulﬀ and Trond Ytterdal, In proceedings of the 23rd NORCHIP Conference, 2005. 21-22 Nov. 2005 Pages 237 - 240 Digital ObjectIdentiﬁer: 10.1109/NORCHP.2005.1597033
Offset | < ± 25mV
Clock Frequency | > 1GHz
Power dissipation | < 222µW
Supply voltage | 0.8 V
Clock signals | 1
High reference | 0.6V
Low reference | 0.2V
Common mode | 0.4V
In short: Shows high speed potential of 90nm CMOS

## Slide 16
Paper 5: Design of a 7-bit 200MS/s, 2mW Pipelined ADC With Switched Open-Loop Ampliﬁers In a 65nm CMOS Technology
    Carsten Wulﬀ and Trond Ytterdal In proceedings of the 25th NORCHIP Conference, 2007. Digital Object Identiﬁer 10.1109/NORCHP.2007.4481042
Highlights:
- 65 nm LP CMOS Technology
- Switched capacitor implementation
- 50fF sampling capacitors
- Six 1.5 bit stages + 1.5 bit Flash
- Four phase clock generator
- Switched open-loop amplifiers
- Transmission gates as switches
- Digital error correction in MATLAB
In short: Demonstrates that open-loop residue amplifiers are an efficient implementation choice for low resolution pipelined ADCs

## Slide 17
Paper 6: Design and Behavioral Simulation of Comparator- Based Switched Capacitor Circuits
    Carsten Wulﬀ and Trond Ytterdal, 26th NORCHIP Conference 2008
Opamp based switched-capacitor
Comparator-based switched-capacitor
In short: Introduces useful design equations for CBSC

## Slide 18
RO, Finite output resistance
TD, Delay of comparator
Make high resistance current source RO>> 1
Make comparator threshold adjustable (Vct)
Gain of amplifier
Overshoot caused by comparator delay

## Slide 19
Paper 7: An 8-bit 60-MS/s 8.5mW Diﬀerential Comparator-Based Switched-Capacitor Pipelined ADC in 90nm CMOS Technology
    Carsten Wulﬀ and Trond Ytterdal, Submitted to Journal of Solid State Circuits

## Slide 20
Evolution of Differential CBSC/ZBSC:
Shin et al, June 18 (submitted january)
A fully-differential zero-crossing-based 1.2V 10b 26MS/s pipelined ADC in 65nm CMOS, VLSI circuits
Brooks, June 6 (may contain differential ZBSC)
Thesis, Circuits and Algorithms for Pipelined ADCs in Scaled CMOS Technologies
Wulff et al, submitted aug 19 2008 (first version of paper June 4)
An 8-bit 60-MS/s 8.5mW Diﬀerential Comparator-Based Switched-Capacitor Pipelined ADC in 90nm CMOS Technology
Brooks et al, probably submitted sept 22
A 12b 50MS/s Fully Differential Zero-Crossing-Based ADC Without CMFB, ISSCC 2009.

## Slide 21
The Multiplying DAC

## Slide 22
Continuous time bootstrapped switch
Comparator with adjustable threshold
High impedance variable current source

## Slide 23
Summary

## Slide 24
Other 8-bit converters above 1MS/s

## Slide 26: http://www.wulff.no/carsten
Papers, thesis, FOM source data, CBSC modeling, Pipelined schematics…