## Slide 1: Implementation of D/A converters in nano-scale CMOS Technology
Carsten Wulff

## Slide 2
Implementation of
  the act of implementing − providing a practical means for accomplishing something
D/A converters
  digital to analog converters − a electronic circuit that transforms a digital signal into an analog signal
in nano-scale
  with transistor lengths less than 100nm
CMOS Technology
  complementary metal oxide semiconductor technology − the dominating technology for electronic circuits

## Slide 3
Information source: Institute of Electrical and Electronics Engineers
http://ieeexplore.ieee.org/

## Slide 4
Part 1: Introduction
  Where are digital to analog converter used?
  What is a digital to analog converter?
  Why choose nano-scale CMOS?
Part 2: Implementation challenges in nano-scale CMOS
  Reduced supply voltage
  Well proximity effect
  Shallow trench isolation stress

## Slide 5: Part 1: Introduction

## Slide 6
Where are digital to analog converters used?
Inside of a cell phone
DAC
ADC
ADC
TX
RX
Digital Processor
Digital Processor
DAC

## Slide 7
Discrete time
Continuous value
Continuous time
Continuous value
Discrete time
Discrete value
Continuous time
Discrete value
Digital
Analog
What is a digital to analog converter?

## Slide 8
Sound examples, how many bits do you need?
Original
2-bit DAC
4-bit
DAC
8-bit DAC
4 levels
256 levels
16 levels

## Slide 9
Do you really need that many bits?
1.5-bit DAC
1.5-bit DAC
Original
Sigma-delta Modulator
Low-pass filter
Notes: 15 minutes

## Slide 10
The most common method of digital-to-analog conversion in nano-scale CMOS technology

## Slide 11
The alternatives
Binary weighted
  Low area
  Low load on digital inputs
  Poor matching
  Large glitches
Thermometer weighted
  Large area
  High load on digital inputs
  Good matching
  Small glitches
DACs are usually implemented as a combination of the two alternatives

## Slide 12
  Why choose nano-scale CMOS?
Broadcom: BCM2153 7.2-Mbps HEDGE 65-nm Multimedia Baseband Processor

## Slide 13: Part 2: Implementation challenges in nano-scale CMOS

## Slide 14
Key papers:
Seo et al, A Low-Spurious Low-Power 12-bit 160-MS/s DAC in 90-nm CMOS for Baseband Wireless Transmitter, JSSC, March, 2007
  ISI, timing synchronization and jitter = switching distortion
  Source degenerated differential pair to improve switch characteristics
  Mismatch caused by Shallow Trench Isolation stress (STI stress)
  Mismatch caused by Well Proximity Effect (WPE)
Savoj et al, A 12-GS/s Phase-Calibrated CMOS Digital-to-Analog Converter for Backplane Communications, JSSC, May, 2008 (90nm)
  RC delay induced mismatch
  Gradient errors
  Using higher than maximum power supply

## Slide 15
Reduced power supply
From ITRS roadmap [http://www.itrs.net]

## Slide 16
Low headroom

## Slide 17
Living outside the rails
Be careful of:
- Voltages during startup
- Reliability, a good idea to run age simulations
[Savoj, JSSC, May 2008]

## Slide 18
Mismatch of transistors
μn = mobility, Cox = εoxε0/tox = Oxide capacitance, VGS = Gate source voltage, VT = threshold voltage
[Razavi,2000]

## Slide 19
Mismatch leads to decreased linearity
Spurious free dynamic range (SFDR)
More mismatch = less SFDR
[Savoy, JSSC, May 2008]

## Slide 20
Well Proximity Effect
[Drennan,CICC,2006]

## Slide 21
Shallow trench isolation (STI) stress
[Diaz, JSSC, March 2003]
Modeled by the parameters sa,sb and sd in SPICE

## Slide 22
Conclusion
Living with low voltage supply
  You can use higher than maximum power supply but you need to be careful
Reducing mismatch from WPE and STI stress
  Place transistors far from well edge (>3μm)
  Simulate on layout early to get the effect of STI stress

## Slide 23
List of papers
Fang et al, A 6-b DAC and Analog DRAM for a Maskless Lithography Interface in 90 nm CMOS, A-SSCC 2006
Cao et al, A 10-bit 1GSample/s DAC in 90nm CMOS for Embedded Applications, CICC 2006
Drennan et al, Implications of Proximity Effects for Analog Design, CICC 2006
Evans et al, Deep Submicron Effects on Data Converter Building Blocks, CICC 2008
Seddighard et al, A 3.6GHz, 16mW Σ∆ DAC for a 802.11n / 802.16e transmitter with 30dB digital power control in 90nm CMOS, ESSCIRC 2008
Pozsgay et al, A Fully Digital 65nm CMOS Transmitter for the 2.4- to-2.7GHz WiFi/WiMAX Bands using 5.4GHz AX RF DACs, ISSCC 2008
Schell et al, A Clockless ADC/DSP/DAC System with Activity Dependent Power Dissipation and No Aliasing, ISSCC 2008
Seo et al, A Low-Spurious Low-Power 12-bit 160-MS/s DAC in 90-nm CMOS for Baseband Wireless Transmitter, JSSC March 2007
Savoj et al, A 12-GS/s Phase-Calibrated CMOS Digital-to-Analog Converter for Backplane Communications, JSSC May 2008 & VLSI 2007
Diaz et al, Process and Circuit Design Interlock for Application-Dependent Scaling Tradeoffs and Optimization in the SoC Era, JSSC March 2003
Drennan et al, Understanding MOSFET Mismatch for Analog Design, JSSC March 2003